## Slide 1: Smart ventilation system for air conditioned rooms and cars

## Slide 2: COMPONENTS:
INTRODUCTION
PROBLEM STATEMENT
IDEA OVERVIEW
MG811 SENSOR
#SPECIFICATIONS
BLOCK DIAGRAM
MODEL DIAGRAM
ADVANTAGES
DISADVANTAGES
VALUE PROPOSITION
BUSINESS VENTURE

## Slide 3: PROBLEM STATEMENT
Over the time if the air-conditioned rooms is in closed condition, there is a possibility of increase in carbon dioxide (CO2) level due to the denser population inside.
If the CO2 level exceeds a safety level of 400 ppm it causes respiratory problems, drowsiness and "sick building syndrome" because of this poor indoor air quality.
It is dangerous to sit inside a locked car. It is even more dangerous when the air-conditioning is on. Car exhaust emits carbon dioxide and carbon monoxide gases (in case the AC is on) that might kill an adult instantly.

## Slide 5: IDEA OVERVIEW :
A solution to provide ventilation to the airconditioned room is to design a system that can exhaust the air inside the room with excess CO2 to the outdoor environment safely through suitable ducts.
The air conditioner which runs continuously can supply the fresh air that circulates inside the room .
The proposed system has a sensor to sense the level of CO2 inside the room
If the density level of CO2 is exceeded than the safety level, few exhaust fans are operated to provide ventilation without opening the door .
This system defines the evacuation of co2 in the buildings and cars for air conditioner.
By constructing this system in air conditioned rooms the co2 level of the room and car is balanced and fresh air is supplied continuously by the air conditioners. By this the working efficiency of the workers inside the rooms increases and it leads to a healthy life.

## Slide 6: MG811 CO2 SENSOR:
FEATURES:
This will sense the gaseous carbon dioxide levels by monitoring the amount of
infrared (IR) radiation absorbed by carbon dioxide molecules.
This type of sensor is used in monitoring indoor air quality, landfills, process control, and
controlled environment horticulture.
The MG-811 is highly sensitive to CO2 and less sensitive to alcohol and CO.
PINOUT:
*VCC: 6V ( You can use a4 AA battery holder for this.
AOUT:Analog Output (voltage decreases as CO2 Levels increase.
DOUT: Digital Output that goes HIGH when the threshold is reached (set the threshold by turning the onboard potentiometer).GND: 0V.

## Slide 7: SPECIFICATIONS:
SPECIFICATIONS | VALUES
Operating voltage | 6V DC
Characteristic gas | CO2
Detection range | 0 – 10000 ppm
Size | 32mm*22mm*30mm
Interface | Gravity analog
Output | 0 – 2 V

## Slide 8: BLOCK DIAGRAM
ARDUINO STARTER KIT
DUCT
(door valve)
EXHAUST FAN
RELAY

## Slide 9: MODEL DESIGN

## Slide 10
Working model for rooms

## Slide 11
Working model for cars

## Slide 12: ADVANTAGES :
Continuous fresh air supply with balanced CO2 level.
Mass leakage of AC by ventilation window is avoided.
It is applicable for workplace like IT companies , hospitals etc...,therefore the working efficiency of the people increases.
Long term ac usage without drowsiness, respiratory problems and dizziness.
It leads to healthy life.

## Slide 13: DRAWBACKS:
Installation cost.
Compared to other split or window air conditioners, an inverter air conditioner is a bit expensive as it comes with unique features.

## Slide 14: VALUE PROPOSITION:
The actual required materials and cost may vary depending on room size – volume of the room.
Materials required for one exhaust fan setup is tabulated.
S.No. | Particulars | Cost in Rs.
1 | Carbon Dioxide Sensor Module | 3500
2 | Arduino Nano CH340 | 300
3 | Exhaust fan (200 mm) | 1300
4 | Flexible Duct pipe (6 inch dia-80 inch length) | 1800
5 | Funnel (9 inch to 6 inch) | 200
6 | Stepper motor with driver | 600
7 | Air vent fan filter cover | 800
8 | Miscellaneous | 1000
 | Total | 9500

## Slide 15
BUSINESS VENTURE

## Slide 16: THANK YOU
ANY QUERIES?